## Slide 1
SOIL
MONITORING
FOR SMART
AGRICULTURE
Sensor-based soil monitoring with real-time measurements, local classification and an offline dashboard
EEG 323 — Instrumentation and Measurement II | Group 2
Department of Electrical and Electronics Engineering · University of Lagos
Supervisor: Dr. Olumide Akintunde Alamu
ESP32
MOISTURE
TEMP
pH
SENSE → PROCESS → DISPLAY

## Slide 2
THE PROBLEM
02
Soil decisions are only as good as the measurements behind them
The project turns three invisible soil conditions into numbers a farmer can act on.
1
Traditional judgment
Farmers may rely on soil appearance, touch and experience when measurement tools are unavailable.
2
Laboratory testing
Accurate testing can require money, time and access to a laboratory — unsuitable for every immediate irrigation decision.
3
Instrument access
Imported or specialised equipment can be difficult to maintain when a component fails.
THE DESIGN RESPONSE
Measure locally.
Process immediately.
Explain the result.
A compact ESP32 instrument combines sensing, calibration, classification and a local user interface in one build.
REAL-TIME
OFFLINE
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 3
AIM & OBJECTIVES
03
A small instrument with a clear job
Measure soil moisture, temperature and pH, then turn readings into usable information.
AIM
Design and implement a sensor-based system that measures soil moisture, temperature and pH, and processes and displays those readings in real time to support irrigation and crop management decisions.
The final build is intended to be portable, maintainable and usable without engineering know-how.
1
Portable
Stable enough to carry to and from the farm.
2
Maintainable
Built from commonly available parts and simple interfaces.
3
Operable
Useful without needing a laptop during normal operation.
SUCCESS LOOKS LIKE
LIVE VALUES
CALIBRATED
LOCAL UI
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 4
MEASUREMENTS
04
Why measure moisture, temperature and pH?
These three measurements describe different parts of the soil environment — water availability, thermal conditions and chemical availability.
1
MOISTURE
41 %
Indicates how much water is available in the root zone and directly supports irrigation decisions.
< 30% DRY · 30–70% GOOD · ≥ 70% WET
2
TEMPERATURE
27.7 °C
Tracks the thermal condition of the soil environment, which affects germination, microbial activity and nutrient availability.
10-bit DS18B20 · 0.25 °C RESOLUTION
3
pH
9.29
Shows the chemical condition of the soil and helps indicate whether nutrient uptake may be limited by acidity or alkalinity.
< 6.5 ACIDIC · 6.5–7.5 NEUTRAL · > 7.5 ALKALINE
In this project, the readings are not presented as raw numbers only — the firmware also translates them into plain-language categories.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 5
SYSTEM ARCHITECTURE
05
One controller, three sensors, two user interfaces
The system is organised as a sensing layer, a processing layer and a display/network layer.
CAPACITIVE MOISTURE
GPIO34 · analogue
DS18B20
GPIO4 · 1-Wire
PH4502C
GPIO35 · via divider
ESP32
DEVKIT V1
Acquire • Calibrate • Classify • Buffer
SH1106 OLED
1.3″ local display over shared I²C
WI-FI SOFT AP
Captive-portal dashboard · multi-device
POWER STAGE
ASM1117 → dedicated 5 V rail for pH front-end
100 µF + 100 nF decoupling
ESP32 logic rail: 3.3 V
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 6
HARDWARE BUILD
06
The build is modular: each part has one job
Keeping sensing, conditioning and display roles separate makes the system easier to debug and maintain.
SENSE
Capacitive moisture v1.2
Analogue soil-water proxy · GPIO34
SENSE
DS18B20
Digital temperature · GPIO4 · 4.7 kΩ pull-up
CONDITION
PH4502C
Conditions the pH electrode signal · 0–5 V stage
PROTECT
10 kΩ / 20 kΩ divider
Scales pH output before GPIO35
DISPLAY
SH1106 1.3″ OLED
Shared I²C local display
POWER
LM2596 + capacitors
Dedicated 5 V rail + transient buffering
Reference circuit diagram from the original build
BUILD PRINCIPLE
Sensors produce signals; the controller never has to “guess” what a pin is supposed to mean.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 7
SIGNAL & POWER INTEGRITY
07
The final build depends on clean signal paths
Most of the engineering detail sits between the sensor output and the ESP32 ADC.
pH SIGNAL PATH
PH4502C
10 kΩ
20 kΩ
ESP32
GPIO35
The divider scales the 0–5 V conditioned signal to an ESP32-safe range near 0–3.3 V while preserving the linear relationship used for calibration.
OTHER PROTECTION / STABILITY DETAILS
4.7 kΩ
DS18B20 1-Wire pull-up
100 µF
Rail reservoir
100 nF
High-frequency decoupling
FINAL WIRING CHECK
✓
Moisture → GPIO34 analogue
✓
DS18B20 DATA → GPIO4
✓
pH → divider → GPIO35
✓
OLED uses shared I²C lines
✓
pH front-end gets dedicated 5 V
✓
ESP32 logic remains at 3.3 V
This separation is what stopped Wi-Fi activity from disturbing the analogue pH measurement.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 8
FIRMWARE
08
Firmware turns raw signals into readable soil status
The main loop runs once per second while calibration, averaging and history buffers make the output more useful than a raw ADC value.
1
ACQUIRE
Sensors → raw values
2
CALIBRATE
Raw ADC → engineering
units
3
CLASSIFY
Moisture / pH → plain
language
4
BUFFER
5 seconds + 1 hour history
5
DISPLAY
OLED + local dashboard
MAIN LOOP · ~1 SECOND
1
Read DS18B20 temperature
2
Read moisture ADC → percentage
3
Read pH from 20 averaged samples
4
Update OLED and dashboard variables
5
Log to the 5-second and 1-hour buffers
CALIBRATION FORMULAS
Moisture % = (ADCraw − ADCair) ÷ (ADCwater − ADCair) × 100
pH = 7.0 − (ADCraw − ADCpH7) × 4.5 ÷ (ADCpH2.5 − ADCpH7)
The calibration points are measured on the actual sensors used in the build.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 9
USER INTERFACE
09
The system works without a PC or router
A local OLED gives immediate feedback; the ESP32 soft AP provides a browser dashboard to phones and laptops.
SH1106 OLED
SMART SOIL MONITOR
TEMP 27.7°C
MOIST 41%
pH 9.29
LOCAL DISPLAY · NO APP REQUIRED
BROWSER DASHBOARD
SMART_SOIL_MONITOR
Join the ESP32 access point from Android, iOS or Windows and open the captive portal.
27.7 °C
TEMPERATURE
41 %
MOISTURE
9.29
PH
24-HOUR HISTORY
5-SECOND BUFFER
NO INTERNET
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 10
DATA INTERPRETATION
10
The firmware explains the measurement
Calibration anchors raw ADC values to known conditions, then the classification layer makes the result understandable at a glance.
MOISTURE CALIBRATION
AIR
2469
WATER
752
41 % → GOOD
The same mapping is applied continuously to the live ADC reading.
pH CALIBRATION
pH 7.0 ADC
2975
pH 2.5 ADC
3790
9.29 → ALKALINE
Twenty samples are averaged before the pH value is updated.
PLAIN-LANGUAGE CLASSIFICATION
MOISTURE
< 30%
DRY
MOISTURE
30–70%
GOOD
MOISTURE
≥ 70%
WET
pH
< 6.5
ACIDIC
pH
6.5–7.5
NEUTRAL
pH
> 7.5
ALKALINE
ACTIONABLE STATUS
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 11
RESULTS
11
Bench testing shows the complete signal chain working
The final build produced stable live values, calibrated classifications and a much faster acquisition loop.
27.7 °C
TEMPERATURE
Stable at 0.25 °C resolution
41 %
MOISTURE
Classified “Good” from calibrated endpoints
9.29
SOIL pH
Classified “Alkaline” from pH 7 and 2.5 points
187 ms
CONVERSION TIME
Down from ~750 ms after using 10-bit DS18B20 resolution
TEST SETUP
Bench testing used the completed sensor assembly and compared the live values produced by the firmware against the intended calibrated behaviour.
LIVE
CALIBRATED
OFFLINE
WHAT THE RESULT MEANS
The important result is not a single “perfect” number. It is that the complete chain — sensor → conditioning → ESP32 → classification → interface — remains coherent and
usable in operation.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 12
LIVE DASHBOARD
The finished system turns sensor readings into usable data
The ESP32 dashboard exposes the current state, recent samples and a longer-term trend view for practical decisions.
EXAMPLE CAPTURE • ESP32 LOCAL WEB DASHBOARD
DATA APPLICATIONS
1
CURRENT STATE
24.5 °C · 100% moisture (Wet) · pH 7.87 (Alkaline)
2
SHORT-TERM HISTORY
The last 20 readings expose stability and variation before a decision is made.
3
TREND + DECISION
The 24-hour buffer can reveal drying, pH movement or temperature changes over time.
LIVE
OFFLINE
LOCAL
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos
11

## Slide 13
APPLICATIONS
13
Where the finished system can be used
The current build is especially suited to situations where local measurements and immediate interpretation are more useful than a remote infrastructure stack.
1
Irrigation decisions
Use live moisture status to support when-to-water decisions rather than relying only on visual judgement.
2
Crop management
Track temperature and pH alongside moisture to build a more complete picture of the root-zone environment.
3
Offline field monitoring
Operate from the ESP32’s local display and Wi-Fi soft AP without a router, internet connection or phone app.
4
Prototype platform
Extend the same architecture with automatic irrigation, more sensor nodes, longer-term logging or additional soil measurements.
NEXT EXTENSIONS
AUTO IRRIGATION
SOLAR + BATTERY
ESP-NOW / LORA
SD / CLOUD LOGGING
NPK SENSING
MOBILE ALERTS
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 14
GITHUB COMPANION
14
A project page should show more than the firmware
The code explains how the controller behaves; this deck explains why the hardware, calibration and user interface were built that way.
HARDWARE
What each sensor does
Why the signal is compatible
Where protection is required
FIRMWARE
Acquisition order
Calibration equations
Classification + buffering
VALIDATION
Measured values
Conversion-time improvement
Faults that were fixed
APPLICATION
How a farmer would use it
What “offline” means
How the platform can grow
REPOSITORY CONTENTS:
Build overview, Wiring , Firmware, Calibration , Test Results , Applications.
SOIL MONITORING FOR SMART AGRICULTURE
EEG 323 • Group 2 • University of Lagos

## Slide 15
CONCLUSION
15
The system met its core objectives
1
Real-time moisture, temperature and pH monitoring in a low-cost embedded build.
2
Calibrated conversion from raw sensor outputs into interpretable soil status.
3
Safe pH voltage matching, dedicated 5 V power and decoupling for stable analogue behaviour.
4
Local OLED + Wi-Fi dashboard with 24-hour history and no router, internet connection or app.
CORE BUILD
ESP32
+
3 sensor inputs
+
local display
+
local dashboard
A compact instrumentation project with a complete sensing → processing → interface pipeline.
From raw voltage to an actionable soil reading.

## Slide 16
Thank you
Soil Monitoring for Smart Agriculture
A practical embedded instrumentation project built to make soil conditions measurable, visible and usable.
Group 2 · EEG 323 Instrumentation and Measurement II
Department of Electrical and Electronics Engineering · University of Lagos